## Slide 1: ECTM: A New Communication Model to Network-On-Chip Schedulability Analysis Mourad Dridi*, Stéphane Rubini*, Frank Singhoff*, Jean-Philippe Diguet† *Université de Bretagne Occidentale, Lab-STICC, France †Université de Bretagne Sud, Lab-STICC, France
24th International Conference on Reliable Software Technologies – Ada-Europe 2019
11-14 June 2019, Warsaw, Poland

## Slide 2: Outline
Introduction
  Context – Network On Chip
  Problem Statement
Exact Communication Time Model (ECTM)
  ECTM for Store And Forward
  ECTM for Wormhole
Implementation and Evaluation
  Accuracy of ECTM
  Scalability of ECTM
Conclusion

## Slide 3: Context -Network On Chip (NoC) Introduction
  Communication infrastructure based on links and routers that interconnect cores providing packet-based data transfer
PE4
PE7
PE2
PE5
PE8
R1
R2
R3
R4
R5
R6
R7
R8
R9
PE6
PE9
PE1
PE3
Scalability
Communication parallelism
Resource contentions between different flows in the network
 communication delays
Notes: So what is the network on chip ?
The netwrk on chip is a communication infrastructure based on links and routers
NoC is widely used since it provide scalability and communication parallelism
But
Sharing ressources between different flows in the network introduce new communication parallelism.
Network-On-chips are widely used in industrial applications
since they provide communication parallelism and reduce energy consumption.

## Slide 4: Problem Statement - Real Time System over NoC Introduction
Real Time System
    Timing constraints of tasks and communications (e.g. deadline) must be enforced during execution.
Real Time System over NoC
To analyze schedulability of periodic tasks in NoC-based parallel architectures, we have to :
  Analyze the task scheduling over processing elements
  Analyze the message communications scheduling over the network.
NoC introduces new communication interferences types (Direct and Indirect interferences)
     Complicate the computation of communication time
Classic multiprocessor real-time scheduling solutions consider worst case communication time instead of the actual delays introduced by the network
     Pessimistic analysis results.
Notes: The use of NoC has been recently extended to real-time systems,
whose execution has to meet temporal constraints.
Communication
delays introduced by the network make the scheduling analysis challenging.
In order to analyse the schedulability of priodic tasks deployed over network on chip
We have
To anlyze the task scheduling
And to analyze the message communication scheduling
So here the probleme that the the new commuincation delays introduced by the network complicate the computation of communication time.
For that
Which lead

## Slide 5: Outline
Introduction
  Context – Network On Chip
  Context – Real Time System
  Problem Statement
Exact Communication Time Model (ECTM)
  ECTM for Store And Forward
  ECTM for Wormhole
Implementation and Evaluation
  Accuracy of ECTM
  Scalability of ECTM
Conclusion

## Slide 6: Exact Communication Time Model (ECTM)
The main goal of ECTM is to assess the schedulability of dependent periodic tasks exchanging messages on NoC.
Architectural Model A set of periodic tasks exchanging messages deployed over a NoC.
Architectural Model
Task Model
Task Mapping
NoC Model
Flow Model
Schedulability
Result
(flow and tasks deadline)
ECTM
R1
R2
R3
PE 1
PE 2
PE 3
1
2
eR1R2
eR2R1
eR2R3
eR3R2
eR3PE3
ePE3R3
eR1PE1
ePE1R1
R

PE
exy
Processing Element
Task
Physical link
NoC Router
Message
Notes: In order to resolve this problem we propose ECTM
ECTM is a noc communication model
From the task mapping , task model Noc model and the flow model , ECTM check the schedulability of the system.
The main goal of ECTM is to assess …
The architectural model is composed of a
In this figure we prsent an exemple of thid mofel
We have three processing element connected by three routers r1 r2 and r3 and several physical links
We assume the system to analyze is expressed by a model of the NoC, a
model of the application as a set of dependent periodic tasks and how such tasks
are deployed on the processing elements.
How to achieve schedulability analysis of the overall system ?

## Slide 7: Exact Communication Time Model (ECTM)
The main goal of ECTM is to assess the schedulability of dependent periodic tasks exchanging messages on NoC.
Architectural Model A set of periodic tasks exchanging messages deployed over a NoC.
Architectural Model
Task Model
Task Mapping
NoC Model
Flow Model
Schedulability
Result
(flow and tasks deadline)
ECTM
R1
R2
R3
PE 1
PE 2
PE 3
1
2
eR1R2
eR2R1
eR2R3
eR3R2
eR3PE3
ePE3R3
eR1PE1
ePE1R1
R

PE
exy
Processing Element
Task
Physical link
NoC Router
Message
How to achieve schedulability analysis of the overall system ?
Notes: So here how ectm achieve the schedulabilty analysis of the overall system
We assume the system to analyze is expressed by a model of the NoC, a
model of the application as a set of dependent periodic tasks and how such tasks
are deployed on the processing elements.
How to achieve schedulability analysis of the overall system ?

## Slide 8: Exact Communication Time Model (ECTM)
ECTM
  Converts NoC flow of messages scheduling to periodic tasks scheduling.
  Each flow of message is transformed to a set of dependent periodic tasks.
Analysis model
  A set of periodic task running on a multiprocessor execution platform.
  We assume a multiprocessor with identical processors and no shared resources.
  Scheduling analysis of such model can be performed with list scheduling algorithms
Simulation
  Simulation time according on feasibility intervals defined by Goossens
Support Wormhole and SAF
  ECTM_Wormhole : Transformations rules for Wormhole NoC
  ECTM_SAF : Transformations rules for SAF NoC
Architectural Model
Task Model
Task Mapping
NoC Model
Flow Model
Schedulability
Result
(flow and tasks deadline)
ECTM
Analysis Model
Task Model
Task Mapping
List scheduling algorithms
Multiprocessors without shared resources
Simulation
Notes: So from the architectural model, ECTM compute an analysis model.
It converts noc flow of messages scheduling to periodic task schduling
Each flow will be transformed to a set of dependent periodic tasks.
So here we present the general approach of ECTM
Next I will give more details about transformation applied by ECTM for Wormhole and SAF NoC

## Slide 9: Transformations Rules of ECTM_SAF
For the SAF mode, each router waits for a full packet to arrive before sending it to the next router
For SAF NoC, ECTM_SAF applies the following rules:
Rule 1 Each router of the architectural model will be removed in the analysis model while keeping all the processing elements.
Rule 2 Each unidirectional link in the network between two routers and processing element of the architectural model will be replaced in the analysis model by a new processing element.
Rule 3 Each flow of the architectural model will be replaced by a set of nb tasks.
  nb :number of links used by the flow.
Notes: So befor explain transformation rules of ectm in saf NoC,
how the packet is transferred in SAF NOC ?
For SAF switching mode,
For that :

## Slide 10: ECTM_SAF - Example
The Architectural Model
R1
R2
R3
PE 1
PE 2
PE 3
1
2
e12
e21
e23
e32
eR3PE3
ePE3R3
eR1PE1
ePE1R1

## Slide 11: ECTM_SAF - Example
The Analysis Model
PE 1
PE 2
PE 3
The Architectural Model
R1
R2
R3
ECTMSAF
PE 1
PE 2
PE 3
1
2
e12
e21
e23
e32
eR3PE3
ePE3R3
eR1PE1
ePE1R1
Rule 1
Notes: Rule 1 Each router of the architectural model will be removed in the analysis model while keeping all the processing elements.

## Slide 12: ECTM_SAF - Example
The Analysis Model
PE 1
PE 2
PE 3
PE PE1R1
PE R1PE1
PE PE2R2
PE R2PE2
PE PE3R3
PE R3PE3
PE R1R2
PE R2R1
PE R2R3
PE R3R2
The Architectural Model
R1
R2
R3
ECTMSAF
PE 1
PE 2
PE 3
1
2
eR1R2
eR2R1
eR2R3
eR3R2
eR3PE3
ePE3R3
eR1PE1
ePE1R1
Rule 2
Notes: Rule 2 Each unidirectional link in the network between two routers and processing element of the architectural model will be replaced in the analysis model by a new processing element.

## Slide 13: ECTM_SAF - Example
The Analysis Model
PE 1
PE 2
PE 3
1
2
PE PE1R1
PE R1PE1
PE PE2R2
PE R2PE2
PE PE3R3
PE R3PE3
PE R1R2
PE R2R1
PE R2R3
PE R3R2
1,1
1,2
1,3
1,4
The Architectural Model
R1
R2
R3
ECTMSAF
PE 1
PE 2
PE 3
1
2
e12
e21
e23
e32
eR3PE3
ePE3R3
eR1PE1
ePE1R1
Rule 3
Notes: Rule 3 Each flow of the architectural model will be replaced by a set of nb tasks.
  nb :number of links used by the flow.
So NoW after applying all rules of ECTM , we apply simulation to the analysis model with list scheduling algorithm in order to decide about the schedulability of the system

## Slide 14: Transformations Rules of ECTM_Wormhole
For Wormhole mode, the packet is divided into a number of fixed size flits. The packet is transferred in a pipeline way and possibly span over multiple routers.
For Wormhole NoC, ECTM applies the following rules:
Rule 1 Each router of the architectural model will be removed in the analysis model while keeping all the processing elements.
Rule 2 Each unidirectional link in the network between two routers and processing element of the architectural model will be replaced in the analysis model by a new processing element.
Rule 3 Each flow of the architectural model will be replaced by a set of nb tasks. (nb = nblink X nbsize)
  nblink: number of links used by the flow
  nbsize: size of message of the flow
Notes: Now we will see the transformations rules for wormhole Network on chip
So at first, how the packet is transferred in wormhole NoC ?
Considering Wormhole Switching Mode, the packet is divided into a number of fixed flit size then it will be transferred in pipelin way. Then the packet can span over multiple routers.
For that ECTM applies the following reules :
We keep the same rules for the first and the second rules.
Rules 3 is different than the third rule considered for SAF NoC

## Slide 15: Outline
Introduction
  Context – Network On Chip
  Context – Real Time System
  Problem Statement
Exact Communication Time Model (ECTM)
  ECTM for Store And Forward
  ECTM for Wormhole
Implementation and Evaluation
  Accuracy of ECTM
  Scalability of ECTM
Conclusion
Notes: Now we move to the implementation and evaluation part.

## Slide 16: Implementation and Evaluation
Implementation into a real-time scheduling simulator “Cheddar”
Evaluation of
      Accuracy
      Scalability
Comparison with Worst Case Communication Time Model (WCCTM)
  WCCTM : a NoC communication model based on worst case communication time analysis
The scheduling analysis is performed with Highest Level First with Estimated Time (HLFET).
Notes: In order to perform evaluation of our approach, we have implemented our communication model into a real time scheduling simulator called Cheddar.
For the evaluation, we have evaluated the accuracy and the scalabilty of ECTM.
In those evaluation, we compared ECTM with WCCTM.
WCCTM is noc communication model based on worst case communication time analyisi for network on chip
Scheduling analysis in those evaluation are performed with the algorithm HLFET
To perform these evaluations, we have
implemented our communication models into a real-time scheduling simulator
called Cheddar [20]. Then, with a rst experiment, we evaluate the accuracy
of ECTM and WCCTM. A second experiment evaluates the scalability of our
approach.

## Slide 17: Accuracy of ECTM Implementation and Evaluation
Chart: Processing Element Utilization
| 0 | 0.08 | 0.16 | 0.24 | 0.32 | 0.4 | 0.48 | 0.56000000000000005 | 0.56000000000000005 | 0.64
ECTM SAF | 100 | 100 | 75 | 50 | 37.5 | 30 | 25 | 15.3846 | 14.2857 | 6.6667
WCCTM SAF | 100 | 80 | 62.5 | 40 | 33.3333 | 28.5714 | 22.2222 | 10 | 7 | 5
ECTM Wormhole | 100 | 100 | 100 | 82 | 75 | 73 | 69 | 62 | 40 | 17
WCCTM Wormhole | 100 | 100 | 80 | 73 | 71 | 69 | 66.6667 | 60 | 33.3333 | 15
Evaluate the rate of schedulable task sets found as schedulable by ECTM and WCCTM models.
Generate randomly 100 sets of dependent periodic tasks using UuniFast.
Random task mapping
Traffic patterns: One-To-One.
Packet size : 4 flits.
 For Wormhole NoCs, ECTM is more accurate than WCCTM with an improvement of 100%.
Notes: The purpose of this evaluation is to make a comparative study between the two
ECTM and WCCTM models in terms of accuracy.
To do so, we evaluate the rate
of schedulable task sets found as schedulable by ECTM and WCCTM models.
In this evaluation we generate randomly 100 sets of dependent …
With an One-To-One trac pattern, the destination node and the source
node are selected randomly using UUniFast.
In this figure we present the rate of schedulable task in fonction of the processing element utillization.
We can see from this figure that ECTM is more accurate than WCCTM.
For wormhole NoC, ECTM is more accurate than WCCTM with 100%

## Slide 18: Accuracy of ECTM Implementation and Evaluation
Chart: Processing Element Utilization
| 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45
ECTM SAF | 100 | 100 | 100 | 88.8889 | 66.6667 | 57.6923 | 40 | 22
WCCTM SAF | 100 | 100 | 29.7872 | 25 | 23.5294 | 20.7547 | 18.8679 | 17.7778
ECTM Wormhole | 100 | 100 | 100 | 100 | 100 | 100 | 88 | 35
WCCTM Wormhole | 100 | 100 | 100 | 100 | 100 | 92.3077 | 77 | 31.3725
Evaluate the rate of schedulable task sets found as schedulable by ECTM and WCCTM models.
Generate randomly 100 sets of dependent periodic tasks using UuniFast.
Random task mapping
Traffic patterns: All-To-One
Packet size : 4 flits.
 ECTM is more accurate than WCCTM with an improvement of 30% for Store-And-Forward NoCs.
Notes: Commentaire oralement pour WCCTM dans le cas All-to-one  bcp d’interference
In this evaluation we keep the same configuration of the last evaluation.
The only difference is the traffic pattern.
In this evaluation, we use all-to-one traffic patterns
In all to one traffic pattern, several messages from different sources will be transferres to same destination which lead important interfeerences and consequently important communication delays.
In this figure, we present the schedulability rate of considered tasks in fonction of pe utilization.
This Fig presents the same results than the last evaluation
ECTM is more accurate
This figure show

## Slide 19
Chart: Number of flow
| 15 | 30 | 45 | 60 | 75 | 90 | 105 | 120
WCCTM | 1.02 | 1.36 | 1.62 | 1.96 | 2.15 | 2.25 | 2.36 | 2.96
ECTM SAF | 1.31 | 1.5 | 1.75 | 2.05 | 2.32 | 2.58 | 2.86 | 3.79
ECTM Wormhole (2 flits) | 1.36 | 1.85 | 2.26 | 2.6 | 2.96 | 3.45 | 5.2 | 6.82
ECTM Wormhole (3flits) | 1.55 | 2.11 | 2.48 | 3.3 | 4.21 | 5.12 | 6.7 | 8.13
 In terms of computation time, WCCTM has a shorter computation time comparing to ECTM with a reduction of
  17% for Store-And-Forward NoCs
  54% for Wormhole NoCs
Measure the computation time of the WCCTM and ECTM transformations.
Generate randomly sets of dependent periodic tasks using UuniFast.
Random task mapping
4x4 NoC
Scalability of ECTM
Implementation and Evaluation
Notes: Now, we move to the scalability evaluation
So in order to evaluate the scalablity of our approcache, we mesured the computation time of WCCTM and ECTM transformation
We keep the same configuration of last evaluations
In this figure we presente the computaion time in fonction of number of flows.
The red curve presents result for WCCTM
The green one presents the result for ECTM for store and forward NoC
Two Blues curve presents the computation time of ECTM for wormhole configuration with 2 flit and 3 flit packet size

## Slide 20: Conclusion
  Problem statement
  New communication delays introduced by the NoC complicate the communication time analysis.
  The communication schedulability is essential to analyze schedulability of periodic tasks deployed over NoC.
  Contribution
ECTM: a NoC communication Model
  Assess the schedulability of dependent periodic tasks exchanging messages on NoC
  Converts NoC flow of messages scheduling to periodic tasks scheduling.
  Implementation available in the Cheddar tool
    http://beru.univ-brest.fr/svn/CHEDDAR/
Result
  ECTM is more accurate than WCCTM
    An improvement of 100% for Wormhole NoC
    An improvement of 30% for Store-And-Forward NoCs
  ECTM need more time to compute the analysis model than WCCTM
    54% for Wormhole NoCs
Notes: Delays introduced by a NoC make the schedulability analysis challenging.
we propose a new NoC communication model called Exact Commu-
nication Time Model (ECTM) in order to analyze the scheduling of periodic
tasks exchanging messages over a NoC.
Our approach supports Wormhole and
Store-And-Forward NoC switching technics.
With ECTM, we perform schedul-
ing analysis with a list scheduling algorithms called HLFET.