## Slide 1: Challenges in Applying Mixed-Criticality Systems to Aircraft Engine Control Systems
Stephen Law, Rolls-Royce
Iain Bate, University of York

## Slide 2: Introduction
Rolls-Royce Control Systems develop DO-178C DAL A, C and E software to control (DAL A) and monitor (DAL C/E) Rolls-Royce aircraft engines.
  All on single core processor devices
Rolls-Royce has had a close collaborative relationship with the University of York for the last 25 years
  Most recently in the SECT-AIR and ENCASE joint research programs

## Slide 3: Why is Mixed Criticality Appealing?
WCET processes are pessimistic, but we would struggle to prove this to a certification authority
  Can we better use this ‘spare’ utilisation?
Mixed Criticality Scheduling allows low criticality tasks to execute on the same target hardware as high criticality tasks
  Allowing low criticality tasks to have deadlines, periods and timing requirements
  Giving a good balance between safety, flexibility and maximising utilisation
Additionally we have a number of tasks we would consider to be high criticality however we can afford for them to be disabled for short periods of time.
  For instance recording error logs in non-volatile memory, a time consuming but still important process.
Principal benefits – Cost & Flexibility.
Notes: Vestal’s work noted that low DAL tasks have been developed against lighter standards, therefore we have less confidence in their WCET
We would extend this to also state we have less confidence in their correct operation
However the potential uses for MCS go beyond simply supporting ‘less important’ tasks.
We have a number of tasks we would consider to be high criticality, because of the effect their failure would have the on the system, however we can afford for them to be disabled for short periods of time. For instance recording error logs in non-volatile memory, a time consuming but still important process.
Therefore it is very important that we address exactly what we mean by a ‘low-DAL’ task
Ultimately it provides two main advantages - cost reduction and flexibility
  Less processors, easier proof of schedulability

## Slide 4: The Vestal Model
Introduces the notion that confidence in a software task’s WCET – C – is proportional to its criticality
  Higher criticality. Higher analysis effort. More pessimistic WCET
  CA ≥ CB ≥ CC ≥ CD ≥ CE
Focusing on a dual criticality system…academic works and models that build off Vestal’s seminal work essentially treat each task as having a WCET for each criticality
  High DAL tasks => CHI and CLO
  Low DAL tasks => CLO
The question is how to utilise the spare execution time – [CHI - CLO]
Notes: Vestal’s work noted that low DAL tasks have been developed against lighter standards, therefore we have less confidence in their WCET
We would extend this to also state we have less confidence in their correct operation
However the potential uses for MCS go beyond simply supporting ‘less important’ tasks.
We have a number of tasks we would consider to be high criticality, because of the effect their failure would have the on the system, however we can afford for them to be disabled for short periods of time. For instance recording error logs in non-volatile memory, a time consuming but still important process.
Therefore it is very important that we address exactly what we mean by a ‘low-DAL’ task
Ultimately it provides two main advantages - cost reduction and flexibility
  Less processors, easier proof of schedulability

## Slide 5
Industrial Point of View
Vestal’s work noted that CLO is obtained against lighter standards, we have confidence in it but we cannot prove it to be sound.
We have developed/tested a low DAL task to the same standard as high DAL task, but gathered less evidence of integrity
  Partitioning must be employed
It is very important that we address exactly what we mean by a ‘low-DAL’ task
  What tasks/operations are appropriate/safe as ‘low-DAL’ tasks?
Equally we need to understand the importance of CLO and CHI
  What restrictions and requirements do these measures place on system integrators?
Notes: Vestal’s work noted that low DAL tasks have been developed against lighter standards, therefore we have less confidence in their WCET
We would extend this to also state we have less confidence in their correct operation
However the potential uses for MCS go beyond simply supporting ‘less important’ tasks.
Therefore it is very important that we address exactly what we mean by a ‘low-DAL’ task

## Slide 6
We have primarily studied AMC+ and the Robust System model
Both models have been implemented around our aircraft engine control system
The robust model is gives controlled graceful degradation
  It allows resilient tasks to exceed CLo a bounded number of times before HighDAL mode is entered
Current State of the Art - Our Understanding
Notes: Remind that AMC will never come back from HighDAL mode

## Slide 7
Robust Mixed Criticality
A robust task is one that can safely drop a non-started job
A fault is measured when one task overruns its CLO
  JF Records the number of Job Failures
An error is registered when one or many tasks fail to comply with their timing requirements
A resilient system is one which employs graceful degradation (if necessary through the control of robust tasks) in order to cope with one or many faults, thus aiming to avoid errors.
Notes: Remind that AMC will never come back from HighDAL mode

## Slide 8: Robust Mixed-Criticality
Normal mode
  F hi-criticality tasks can exceed CLO
Resilient mode
  Up to M tasks can exceed CLO
  Each robust task can skip up to S jobs
High-criticality mode
  Low-criticality tasks are not released
On an idle tick the counters for jobs skipped (JF) are reset
If CHi is exceeded then there is a power cycle

## Slide 9
Results From Porting Existing System
An existing Rolls-Royce control system was ported to the Robust Mixed Criticality model.
  >40% additional utilisation
  Identification of CLO and CHI aligned well to our processes
  In particular we studied the application of a monitoring task responsible for writing to NVM
    Robust and low-DAL
    Responsible for writing data from a queue to NVM
    Able to drop some jobs, then need to run normally to catch up
    Can we be confident its write queue will not overflow?
Notes: Remind that AMC will never come back from HighDAL mode

## Slide 10
Assessing Low Criticality Service
Current static schedulability analysis confirms
  High-criticality tasks always meet their deadlines
  Low-criticality tasks meet their deadlines when jobs are released and completed
  If jobs are allowed to be skipped, then the number is bounded
Many academic papers have looked at improving low DAL service
None (to our knowledge) have identified ways to quantify it
We want to know
  What is the minimum gap between entering high-criticality mode?
  The max jobs skip allow us to guarantee from a normal level the buffers don’t overflow
  The minimum gap then allows us to guarantee the buffers return to normal
Notes: Remind that AMC will never come back from HighDAL mode

## Slide 11
A GSN supported statistical approach built around a scheduler simulator, seeded with real data, and updated throughout the software development process
Assessing Low Criticality Service
Confidence
Likelihood
Correctness
Acceptability
Notes: Remind that AMC will never come back from HighDAL mode

## Slide 12
Assessing Low Criticality Service
Using a scheduler simulator allows early design time analysis
  Simulator uses real execution time profiles
How can we have confidence that the simulator has observed a large enough sample of the search space?
How can we have confidence that continued testing will not reveal new results?
Confidence
Blue line is the average
Red line is the minimum
Notes: Remind that AMC will never come back from HighDAL mode

## Slide 13: Assessing Low Criticality Service
Simulations parallelised so significant data can be obtained
Rather than just looking at the results convergence was assessed
  Take X% of the simulation results and compare to the rest
Use confidence intervals
  How confident we are that the minimum gap is greater than Y%?
and chi-squared test
  Do the same come from the same distribution?
and Earth Movers Distance
  How different are the distributions?
Confidence
Notes: Remind that AMC will never come back from HighDAL mode

## Slide 14
Assessing Low Criticality Service
How often do we come close to seeing an error?
If an error has been observed, what is its frequency of occurrence?
If an error has not been observed, use a fitted distribution to assess an exceedance probability
Likelihood
Notes: Remind that AMC will never come back from HighDAL mode

## Slide 15
Assessing Low Criticality Service
How can we be sure the simulation is correct?
  Simulation offers a route to fast, iterative, repeatable testing… provided the simulation is correct
Seeded and configured with real system parameters
  Real task attributes
  Execution times for tasks obtained through systematic testing
  Accurate model of the scheduler including overheads
As control system matures, the simulation is supplemented with, and reviewed against real test campaign data
Correctness
Notes: Remind that AMC will never come back from HighDAL mode

## Slide 16
Assessing Low Criticality Service
Are the results acceptable?
Our case study identified that 40% additional utilisation could be added to the process, which could be expected to complete its operation, without error, in 99.995% of cases
  But… that’s potentially 360 low DAL timing errors per hour…
Is this good enough…?
  Depends on the task’s system requirements
  If not, the system can be refined, with the simulation easily repeated. Hopefully, at an early point in the design lifecycle
Acceptability
Notes: Remind that AMC will never come back from HighDAL mode

## Slide 17
Conclusions
The potential for utilising mixed criticality scheduling techniques is high
  Cost and flexibility
However, the academic literature (to our knowledge) does not presently offer ways to quantify, or prove, the service afforded to low DAL, or robust, tasks.
This paper has integrated a robust mixed criticality scheduler with a real industrial control system, presenting real world results
The paper suggested an approach that could be used to allow a system integrator to gain confidence
Notes: Remind that AMC will never come back from HighDAL mode